## Slide 1: Function Specification
  This file includes:
  General rules for coding
  Defines main flow
  Defines desired features, desired output for each module
  Author: Huy Vu
  Date: 16th Mar, 2017

## Slide 2: Design & Assigned Task
RPi 3
All
Main program
Huy Vũ
Touch
TBD
Motor high
No change
Uno
TBD
Motor low
No change
Height
TBD
SpO2
Chung
Scale
Huy Lê
Blood Pressure
Viễn
Temperature
TBD
Audio
Huy Vũ
Network
C + Q + L
Bluetooth
Chung
Connect server (WiFi)
Quang + Lý
Utility
C + Q + T + L
Android app
C + Q + T + L
User profile
Thành
Bluetooth
Chung
Connect server
Quang + Lý
Server
Quang + Lý

## Slide 3: General rules
Function name:
  module_functionname(arg1, arg2…)
    The name should be meaningful
    The module name is lower case
    Ex: spo2_init(); scale_calibration(); …
Variable name:
  Meaningful
  Ex:

## Slide 4: Main flow
Main program will be written in Python, reasons:
  Add new module easily
  Raspbian and most unix distros support python natively
  Merge whole project easily
Other modules can be written in any languages, the output of each module is an executable file
main() will call processes in desired order, OS will manage these processes.
inter-process communication: via files

## Slide 5: Main flow
main() start
Setup touch
Setup wifi, connect server, Bluetooth, audio, power blood pressure machine,
Init remain modules
Uno measure height
Pi measure Temperature, scale, SpO2, blood pressure
Get outputs
Send data to server
END
Sends output to Pi +
Voice message
START +
Voice message
Voice

## Slide 6: Main
Init Pi, connect wifi
Call modules
Handling inter-process communication (via files)
Huy Vu + Huy Le

## Slide 7: Uno
Input:
  Pi-side: wait for a file name touch_finish
  Uno-side: Get start signal from Pi
Output:
  Send height to Pi, store height (string) in a file name height_result
TBD

## Slide 8: SpO2
Input:
  wait for a file name spo2_start
Output:
  Put user’s SpO2 data (string) in file name spo2_result
Chung

## Slide 9: Scale
Input:
  wait for a file name scale_start
Output:
  Put user’s weight (string) in file name scale_result
Huy Le

## Slide 10: Blood pressure
Input:
  wait for a file name bp_start
Output:
  Put user’s blood pressure (string) in file name bp_result
Vien

## Slide 11: Temperature
Input:
  wait for a file name temp_start
Output:
  Put user’s temperature (string) in file name temp_result
TBD

## Slide 12: Audio
Input:
  Pre-record voice message
  Wait for touch_finish
  Wait for result files
Output:
  Output the message to speaker
Huy Vu >> This module will be implemented in python

## Slide 13: Bluetooth
Input:
  none
Output:
  Pair the system and user’s phone
Chung

## Slide 14: Pi Connect server via WiFi
Input:
  Wait for files: height_result, spo2_result, scale_result, bp_result, temp_result
Output:
  Send those result to server
  Create a file name wifi_finish
Quang + Ly

## Slide 15: Touch
Input:
  None
Output:
  Create a file name touch_finish
TBD

## Slide 16: Utilities
Server
Handle result from Pi
Quang + Ly
Android app
Bluetooth
User profile
Store user data (ID, name…)
Store user result (height, weight, spo2, blood pressure, temperature)
See above Bluetooth slide
Ask mentor for more information )
Chung
Thành
Connect with server to show result on android phone
Quang + Ly

## Slide 17
Member | Task
Huy Vũ | Main program, Audio
Huy Lê | Main program, Scale
Chung | SpO2, Bluetooth (Pi side), Bluetooth (Android side)
Thành | User profile
Viễn | Blood Pressure
Lý | Server, Connect server via wifi (Pi), connect server (android)
Quang | Server, Connect server via wifi (Pi), connect server (android)
Summary

## Slide 18: This file can be updated by any member’s request. This is not final version.

## Slide 19: END
All corrections, suggestions, contributions are welcome