## Slide 1: Function Specification
  This file includes:
  General rules for coding
  Defines main flow
  Defines desired features, desired output for each module
  Module code
  Author: Huy Vu
  Date: 16th Mar, 2017

## Slide 2: Design & Assigned Task
RPi 3
All
Main program
Huy Vũ
Touch
Lý
Motor high
Lý
Uno
Viễn
Motor low
No change
Height
Viễn
SpO2
Chung
Scale
Huy Lê
Blood Pressure
Viễn
Temperature
Quang + Lý
Audio
Huy Vũ
Network
C + Q + L
Bluetooth
Chung
Connect server (WiFi)
Quang + Lý
Utility
C + Q + T + L
Android phone
Chung + Thành
User profile
Thành
Bluetooth
Chung
Server
Quang + Lý

## Slide 3: General rules
Function name:
  <module-code>_<functionname>(arg1, arg2…)
    The name should be meaningful
    The module name is lower case
    Ex: spo2_init(); scale_calibration(); …
Variable name:
  Meaningful
Remember to comment in source code

## Slide 4: General rules
Main program will be written in Python, reasons:
  Add new module easily
  Raspbian and most unix distros support python natively
  Merge whole project easily
Other modules can be written in any language, the output of each module is an executable file and some file used for communication
inter-process communication: via files

## Slide 5: Main flow
main() start
Setup touch
Uno measures height
Pi measures
Prepare outputs
Send data to server
END
Setup
Power BP Machine on
Initialize SpO2, Scale, Temperature module
Pi measures SpO2
Get blood pressure result
Scale
Temperature
Audio
Bluetooth
Uno
Sends
output
to Pi
START +
Voice
Voice
Voice

## Slide 6: Main
Huy Vu
Description:
  Initialize Pi
  Call modules according to system flow
  Handling inter-process communication
Output:
  Program: main.py, main_class.py (header file)

## Slide 7: Audio
Huy Vu >> This module will be implemented in python
Description:
  Input: some mp3 files
  Initialize audio, then generate audio_finish
  Play mp3 according to current step.
Output:
  Program: audio
  File: audio_finish

## Slide 8: Bluetooth
Chung
Description:
  Pair Pi and the connecting Android phone
  Get android phone mac address, store in bluetooth_result
  When finish, generate bluetooth_finish
Output

## Slide 9: Touch
Lý
Description:
  Initialize and control the hand-placing platform
  After initialize, generate touch_finish
Output:
  Program: touch
  File: touch_finish

## Slide 10: Uno
Viễn
Description:
  Initialize then wait for a file name touch_finish (uno_start), then send START signal to Uno.
  Uno will drive the motor, measure height, then send back to Pi
  Pi store that result in a file name height_result, generate a file name uno_finish
  SPI interface
Output:
  Program: uno
  File: height_result, uno_finish

## Slide 11: Scale
Huy Le
Description:
  Initialize then wait for a file name uno_finish
  Measure weight
  Store result in scale_result, generate scale_finish
Output:
  Program: scale
  File: scale_result, scale_finish

## Slide 12: Temperature
Description:
  Initialize then wait for a file name uno_finish
  Measure temperature
  Store result in temp_result, generate temp_finish
Output:
  Program: temp
  File: temp_result, temp_finish

## Slide 13: SpO2
Chung
Description:
  Initialize then wait for a file name scale_finish AND temp_finish
  Measure the SpO2
  Store that result in file name spo2_result, generate spo2_finish
Output:
  Program: spo2
  File: spo2_result, spo2_finish

## Slide 14: Blood pressure
Viễn
Description:
  Has two program: bpressure_poweron, bpressure
  bpressure_poweron will power on the bpressure machine, initialize the auto-mechanical
  after that, generate file bpressure_poweron_finish
  bpressure will measure when spo2_finish exists
  Store result in bpressure_result, generate bpressure_finish
Output:
  Program: bpressure_poweron, bpressure
  Output: bpressure_result, bpressure_finish

## Slide 15: Pi Connect server via WiFi
Quang + Lý
Description:
  Send data to server when wifi_start exists
  Generate file wifi_finish
Output:
  Program: wifi
  File: wifi_finish

## Slide 16: Utilities
Server
Handle result from Pi
Quang + Ly
Android app
Bluetooth
User profile
Store user data (ID, name, mac addr…)
Store user result (height, weight, spo2, blood pressure, temperature)
See above Bluetooth slide
Ask mentor & server team for more information )
Chung
Thành

## Slide 17
Module | Code
Audio | audio
Bluetooth | bluetooth
Blood pressure | bpressure
Scale | scale
SpO2 | spo2
Temperature | temp
Touch | touch
Uno | uno
Connect server (wifi) | wifi
Module code (for implementing)

## Slide 18
Summary
Member | Task
Huy Vũ | Main program, Audio
Huy Lê | Scale
Chung | SpO2, Bluetooth
Thành | User profile
Viễn | Blood Pressure, Uno
Lý | Server, Connect server via wifi (Pi), temperature, touch
Quang | Server, Connect server via wifi (Pi), temperature, touch

## Slide 19: This file can be updated by any member’s request. This is not final version.

## Slide 20: END
All corrections, suggestions, contributions are welcome